## Slide 1: Slow-Control Meeting
Zulkaida Akbar
07/08/2020

## Slide 2: Background
I am beginner on LabView
Misha’s templates are very helpful (we don’t need to build the VI Lib from scratch)
I want to share my experiences on implementing the templates for my particular instrument

## Slide 3: Instrument
Pressure sensor for the outer vacuum of the magnet-dewar
Sensor: Pfeiffer-PKR 361
Read out/Controller: Pfeiffer-TPG 361
Single Channel

## Slide 4: VI Library
The instrument manual provides many commands for “setting” and “getting” (Reading the pressure, set/read the working gauge, unit of the measurement, etc..)
Today I just show one basic functionality which is reading the pressure
The library consist of Visa initialization, Visa close, get pressure

## Slide 5
VISA Initialization
Misha’s template: thcd_visa_init.vi
My instrument: tpg361_visa_init.vi
COM Protocol: RS485

## Slide 6
VISA Close
My instrument: tpg361_visa_close.vi

## Slide 7
Main VI (Get Measurement)
Misha’s template: thcd_get_uom.vi
My instrument: tpg361_get_p.vi

## Slide 8
Command
Get measurement flow
Transmit command (contacting the device)
Receive acknowledgment from the device
Transmit command to get the measurement value
Receive measurement value

## Slide 9
Transmit Command
Acknowledgment status indicator
Transmit Command
String manipulation to get the pressure value & overall status indicator

## Slide 10
Front panel

## Slide 11: Summary
Start with one basic functionality (get pressure reading)
See Misha’s example (thcd_get_uom.vi)
Read the device’s manual
Build (modify) the VI following Misha’s example (In my case a lot of works are string manipulation)
Use NI Max to establish the connection with the device

## Slide 12: Comment
Remember to save in 2018 version
USB comm vs RS 485
There is ethernet protocol -> explore because better
How to make sure it is in the correct setting (unit, etc, …)
Type of working gauge (pirani/cold cathode)
Status indicator if its wrong -> Implemented!!