## Slide 1: NMR with Machine Learning
Devin Seay, Ishara Fernando, Dustin Keller

## Slide 2: Outline
NMR Measurements w/ (Liverpool) Q-Meter
Deuteron lineshape and simulations
Why Artificial Neural Networks (ANN)?
Preliminary results
Observations & Outlook

## Slide 3: What is Nuclear Magnetic Resonance (NMR)?
Nuclear Magnetic Resonance, or NMR, is the physical phenomenon that occurs when a constant magnetic field is applied to nuclei at resonance which is perturbed by a weak oscillating magnetic field, which causes the nuclei to respond by producing an electromagnetic signal with a frequency characteristic of the magnetic field of the nuclei.
In the case of this project, we are using NMR to study the inner structure of the Deuterium nucleus (Deuteron).

## Slide 4: Q-Meter Based NMR
Using a non-destructive continuous wave phase-sensitive detector (ex., a Q-meter), is required to make accurate measurements of polarization in scattering experiments

## Slide 5: NMR Measurements with Q-Meter
Q-meter couples to the magnetic susceptibility of target material ( e.g. Solid Ammonia)
  Signal passes through λ/2 length cable (358.0 cm for 5T), so the continuous wave NMR signal has a tuning range of λ/2 to 7λ/2
  With a frequency range of 3-300 MHz
Within these limits, we expect a linear relationship between Polarization and scale (ideal settings gives 2% relative error)

## Slide 6: Q-Meter Design
Q-meter parameters:
  U, the input voltage (V), calculating using:
  , the tuning capacitance
  , the trim, is the half-integer length of the such that each full-length segment of a cable is
  η, the filling factor of the coil, is the level of coupling of spins in the target material to the sampling coil
  φ, the phase offset, expressed in the form: φ(ω) =a+bω+φ
  , is the stray capacitance, including parasitic capacitance
    True C calculated as C(ω) = (20*)*
Figure reference: Nuclear Instruments and Methods in Physics Research A324 (1993)
Q-meter circuitry
NMR circuitry

## Slide 7
7
Q-meter Equations

## Slide 8: NMR System

## Slide 9: Deuteron Lineshape
The Deuteron lineshape has two corresponding absorption lines, and , which are associated with the analytical function for ε = ±1
  These absorption lines arise due to the interaction of the Deuteron’s quadrupole moment with the electric field gradient (EFG), which creates non-degenerate eigen states in the energy levels.
  Because ND3 lacks cubic symmetry, the previously mentioned interaction breaks degeneracy of energy transitions  quadrupole splitting leading to two overlapping absorption lines in the NMR spectra (Pake Doublet).
  The intensity of the signal, and thus the polarization, is a function of the angle θ between the EFG and the holding field.
  This Pake doublet is particular to spin-1 material without cubic symmetry (Deuteron, Butanol). With it, such as in LiD, we obtain a Guassian-like lineshape
Green:
Blue:
Red: Lineshape
https://doi.org/10.1016/S0168-9002(97)00317-3

## Slide 10: Deuteron Lineshape
The Pake Doublet is mathematically described by the energy levels:
The peaks correspond to the principal axis of the coupling interaction being perpendicular (θ = π/2) to the magnetic field.
The opposing end (the pedestal) corresponds to the configuration when the principal axis of the coupling interaction is parallel (θ = 0) to the magnetic field
Green:
Blue:
Red: Lineshape

## Slide 11: Real Example of Deuteron Signal
Court, G.R. & Houlden, Michael & Bültmann, S. & Crabb, D.G. & Day, Day & Prok, Y.A. & Penttila, S.I. & Keith, Christopher. (2004). High precision measurement of the polarization in solid state polarized targets using NMR. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment. 527. 253-263. 10.1016/j.nima.2004.02.041.
Notes: There are still challenges with noise even with best techology

## Slide 12: Measuring Polarization
Thermal Equilibrium (Previous technique)
  When we have the lattice (L-Helium) and the target material at the same temperature, we can obtain the TE polarization by the equation:
  Then for any polarization not in TE
    , where C is the calibration constant calculated
Using TE method comes with considerable error (~ 7% relative error) from the change in area of the TE signal and the fitted signal.
https://doi.org/10.1016/j.nima.2013.06.103

## Slide 13: Limitations for Deuteron polarization determination
The Liverpool Q-meter system allows for relative accuracy a deuteron signal’s polarization (error of about 1%). However, in the experimental setting, this is far worse, especially at low polarizations. Normally in the experimental setting, we’d expect a relative uncertainty of about 4-6%
Sources of error:
  cable length (Deuteron’s small magnetic moment can lead to large Q-curves)
  Q-meter configurations (calibration constant)
  Changes in Radiofrequency (RF) environment
  Temperature Change
  Statistical errors dependent on DAQ
Here, we’re concerned with trying to overcome complications caused by the first and third sources
https://doi.org/10.1016/j.nima.2013.06.103.

## Slide 14: Why Artificial Neural Networks (ANN)?

## Slide 15: What is ANN?
Neural networks learn (or are trained) by processing examples, each of which contains a known "input" and "result," forming probability-weighted associations between the two, which are stored within the data structure of the net itself.
The training of a neural network from a given example is usually conducted by determining the difference between the processed output of the network (often a prediction) and a target output. This difference is the error.
The network then adjusts its weighted associations according to a learning rule and using this error value. Successive adjustments will cause the neural network to produce output which is increasingly like the target output.

## Slide 16: Benefits of ANN in NMR
Allows us to operate outside the Q-meter design parameters and accurately extract polarization measurements (Around 1-2% relative error)
Even with added Gaussian noise to make the deuteron signal less discernable, ANN can be trained to filter out the noise and measure the true polarization of a signal by noise that has an SNR of 10 and below

## Slide 17: Neural Networks: A Possible Solution
By training a neural network (NN) on sample data that replicates experimentally accurate noise levels that evolve through time, we can go beyond the capability of the Q-meter and make up for where it lacks.
Using to optimize precision and accuracy, regardless of Signal-to-Noise Ratio (SNR)
SNR: ratio of maximum of amplitude of signal to maximum of amplitude of noise, represents how overwhelming the noise is
In our case, we simulate and extract the signal over 500 data bins
By training an NN to associated a specific polarization with its associated signal over 500 data bins, we can accurately predict polarization for a given noisy signal

## Slide 18: NN Architecture
Input layer: 500 nodes (each input node is one of 500 frequency bins of a sample signal)
5 Hidden layers (varying node sizes)
Output layer: 1 node  polarization!
Optimizer used: Adam, a popular optimizer for most general purposes
Relu6 is used as an activation for layer up until the output layer
  Sigmoid is used in output layer to return a value between 0 and 1.
Regularizer L2 is used on each layer
Trained for 1000 epochs
Not to scale

## Slide 19: Sample Data Creation
NN is trained on sample data that varies P from 0-1
  Noise is generated as a Gaussian distribution with standard deviation
    Standard deviation is varied from 0 to roughly , a deviation well above the size of the signal
  4 Million events are created to train on

## Slide 20: Preliminary Results

## Slide 21: Training the Neural Network & Preliminary predictions
Sample data is created with noise added for a given cable length n and level of polarization P between 0 and 1. NN is then trained to recognize lineshape of particular P within the noise over 500 epochs
Histogram of percentage difference (%) predicted by NN for 100K sample events between 0%-100% polarization
SNR: 15-40
Accuracy, how close sample data is to true value : 99.835%
Precision, how much sample data varies from true value: 99.438% (width of predicted P's)
Histogram of Percentage Difference: μ=.165%, σ=0.562%

## Slide 22
Voltage
Notes: Predicted polarization is regraphed via the analytic lineshape function across R, a dimensional parameter expressed as , where is the Lamour frequency for the Deuteron
Predicted polarization is regraphed via the analytic lineshape function across R, a dimensional parameter expressed as (ω − ω_𝐷)/ω_𝐷 , where ω_𝐷is the Lamour frequency for the Deuteron

## Slide 23
Voltage

## Slide 24
Voltage

## Slide 25: Prospective Outlook and Future Plans
ANN can allow for the efficient filtering of background noise from deuteron signal (could also be applied to any NMR signal)
The adaptability of the ANN allows for changes in baseline and scanning range of an NMR to quickly and easily be considered
For the future: optimize the ANN for smaller polarizations to increase precision and accuracy

## Slide 26: Thank you!
This work was supported by DOE contract DE-FG02-96ER40950